# QStarz BT-Q810 bluetooth GPS muis
Fabrikant: Qstarz. De handleiding is zeer kernachtig (om het eufemistich uit te drukken): rechstreeks op qstarz.com of lokaal op www.vdmeulen.net.
## Testprogramma's
- Test voor op PC
- Test voor windows CE (PDA)
## Reviews
- Pocket PC reviews
- Pocketinfo.nl
- GPS plaza
## Specificaties
General
GPS Chip	MTK GPS Module
GPS Protocol	NMEA-0183 (V3.01) - GGA, GSA,GSV, RMC(default),GLL, ZDA, VTG (optional), Band rate 115200 bps Data bit : 8, stop bit : 1(Default)
Frequency	L1, 1575.42MHz
C/A Code	1.023MHz chip rate
Channels	32 CH all in view tracking
Antenna (Intemal)	Built-in patch antenna with LNA
Sensitivity	Tracking -158 dBm
Certification	CE/FCC/BQB/RoHS
Acquisition Rate
Cold Start	39 sec, average
Warm Start	36 sec, average
Hot Start	1 sec, average
Reacquisition	< 1 sec
Power
Battery	Built-in rechargeable 1000mAh Li-ion battery
Consumption	Acquisition:55.1mA(only baseband +RF IC) Tracking:30.3mA Typical(only baseband +RF IC)
Operation Time	25hrs, after fully charged, in continuous
Charging time	3hrs. (Typical)
Environmental
Operating Temperature	-10°C ~ +60°C
Storage Temperature	-20°C ~ +60°C
Charging	0°C ~ +45°C
Accuracy (none DGPS)
Position	Without aid: 3.0m 2D-RMS <3m CEP(50%) without SA(horizontal) DGPS (WAAS, EGNOS, MSAS, RTCM): 2.5m
Velocity	Without aid: 0.1m/s, DGPS(WAAS, EGNOS, MSAS, RTCM): 0.05m/s
Time	50 ns RMS
Dynamic Conditions
Altitude	< 18,000 M
Velocity	< 515 m/sec
Acceleration	< 4G
Update	1Hz as default (Up to 5Hz - optional)
Interface
Bluetooth	V1.2 compliant (SPP profile) Class 2 (15 meters in open space) Frequency: 2.4~2.4835 GHz
Power On/Off	Slide switch
Power Charge	Mini USB
LED function	Bluetooth connection, Navigation Status, and Battery/charger status
Device Size	72.2 (L) X 46.5 (W) X 20 (H) mm
Accessories
Power adaptor, Car Charger, Rechargeable Battery

## Betekenis Leds
Led	Kleur	Knipperend	Aan	Uit
Batterij	Rood	Batterij bijna leeg
“”	Groen	Klaar met laden	Aan het laden
Bluetooth	Blauw	Per 1 sec.: verbinding; per 5 sec.: spaarstand (tomtom uit?)	Geen verbinding/partnership opzetten	Muis staat uit
GPS	Oranje	Heeft fix, naviagtie mogelijk	Geen fix	Muis staat uit